## Slide 1: Wind Energy Project Report (Power curve modelling and performance evaluation)
Prepared By:
Nitesh Kumar & Adaiyibo Kio

## Slide 2
Summary

## Slide 3
Data Preprocessing
Data Exploration and visualization laid the basis to filter important states of features. The three major ones are:
Turbine State – 5 2) Power Limitation – 0 3) Data Valid – 1
The above filtering reduced the data-set by approximately 33%.
Modelling
The analysis was carried out on 1 minute averaged data and 10 minutes averaged data using KNN.
The set of input variables (predictors) are listed on the next slide.
Cross validation RMSE is used to select the best model. A forward selection strategy is used.
Data and processing

## Slide 4
Variable | Notation Used
Wind Speed | W
Wind Direction | D
Generator Speed | G
Ambient temperature | T
Nacelle Position | Nac
Blade Angle | Ang
Power Limitation | PL
Data Valid | DV
Turbulence Intensity | I
Note :–
Turbine blade angle is taken as the average of blade angle 1, 2 and 3
Results are presented in normalized state i.e (RMSE/Rated Power )*100
Group 1 – Power Limitation : 0 and Data Valid : 1
Group 2 - Power Limitation : 0 and Data Valid : 0
Group 3 - Power Limitation : 1 and Data Valid : 0
Model 1 – Include G and Ang , Model 2 – Exclude G and Ang
New
addition

## Slide 5
Model 1: Using G
Model | Turbine – 34(2016) RMSE(%) | Turbine – 34(2018) RMSE(%) | Turbine – 61(2018) RMSE(%)
KNN – 10 mins (average) | 2.07% | 1.98 % | 1.70 %
Gaussian – 10 mins (average) | 1.63% | 1.96% | 1.40%
BINNING – 10 mins (average) | 3.93% | 4.37% | 3.94 %
% reduction from Binning(KNN) | 47% | 55% | 57%
% reduction from Binning(Gaussian) | 58% | 55% | 64%
Best variable sets | W, G, T, Ang | W, T, G | W, T, G, I

## Slide 6
Model | Turbine – 34(2016) RMSE(%) | Turbine – 34(2018) RMSE(%) | Turbine – 61(2018) RMSE(%)
KNN – 10 mins (average) | 3.18% | 2.50 % | 2.93 %
Gaussian – 10 mins (average) | 3.15% | 2.54% | 2.84%
BINNING – 10 mins (average) | 3.93% | 4.37 % | 3.94 %
% reduction from Binning(KNN) | 19% | 43% | 26%
% reduction from Binning(Gaussian) | 19% | 42% | 28%
Best variable set | W, T, I | W, T | W, T, I
Model 2: Not using G

## Slide 7
YEAR - 2016
Turbine Number - 34
Bin-wise RMSE reduction

## Slide 8
Binwise RMSE
RMSE
(kW)
Wind Speed (m/s)

## Slide 9
RMSE
(kW)
Power (kW)
Binwise RMSE

## Slide 10
YEAR - 2018
Turbine Number - 34
Bin-wise RMSE reduction

## Slide 11
Binwise RMSE
RMSE
(kW)
Wind Speed (m/s)

## Slide 12
RMSE
(kW)
Power (kW)
Binwise RMSE

## Slide 13
YEAR - 2018
Turbine Number - 61
Bin-wise RMSE reduction

## Slide 14
RMSE
(kW)
Wind Speed (m/s)
2016

## Slide 15
RMSE
(kW)
Power (kW)